## Slide 1
Network Topology Exercise A V1.0
From
Routing Tables
to
Network Topology

## Slide 2: Network Topology Exercise A
You need to understand the contents of the routing table to determine:
  the Topology of the network
  if there is a Problem with the operation of the routing protocol

## Slide 3: Routing Table Entries – show ip route
The contents of the routing table:
Link local route interfaces - Added to the routing table when an interface is configured. Shows IP address of the Interface.
Connected interfaces – directly connected networks Added to the routing table when an interface is configured and active.
Static routes - Added when a route is manually configured and the exit interface is active.
Dynamic routing protocol – remote networks Added when RIP, EIGRP or OSPF are implemented and networks are identified.
Notes: 1.3.1.2 Routing Table Sources

## Slide 4: Tasks
Given Routing Tables for R1, R2 and R3
Draw a Network Topology Diagram
  Show all interfaces with their ip addresses
  Show all LAN subnets with their subnet addresses
  Show all Serial subnets with their subnet addresses
Answer Questions on the information contained in the routing tables
Notes: 2.2.1.6 Verify a Static Route

## Slide 5: R1 Router - Routing Table
R1# show ip route
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
C 10.1.1.0/30 is directly connected, Serial0/0/0
L 10.1.1.1/32 is directly connected, Serial0/0/0
R 10.2.2.0/30 [120/1] via 10.1.1.2, 00:00:21, Serial0/0/0
172.30.0.0/16 is variably subnetted, 2 subnets, 2 masks
C 172.30.10.0/24 is directly connected, FastEthernet0/1
L 172.30.10.1/32 is directly connected, FastEthernet0/1

## Slide 6: R2 Router - Routing Table
R2# show ip route
10.0.0.0/8 is variably subnetted, 4 subnets, 2 masks
C 10.1.1.0/30 is directly connected, Serial0/0/0
L 10.1.1.2/32 is directly connected, Serial0/0/0
C 10.2.2.0/30 is directly connected, Serial0/0/1
L 10.2.2.2/32 is directly connected, Serial0/0/1
R 172.30.0.0/16 [120/1] via 10.2.2.1, 00:00:23, Serial0/0/1
[120/1] via 10.1.1.1, 00:00:09, Serial0/0/0
209.165.201.0/24 is variably subnetted, 2 subnets, 2 masks
C 209.165.201.0/24 is directly connected, FastEthernet0/0
L 209.165.201.1/32 is directly connected, FastEthernet0/0

## Slide 7: R3 Router - Routing Table
R3# show ip route
10.0.0.0/8 is variably subnetted, 3 subnets, 2 masks
C 10.2.2.0/30 is directly connected, Serial0/0/1
L 10.2.2.1/32 is directly connected, Serial0/0/1
R 10.1.1.0/30 [120/1] via 10.2.2.2, 00:00:23, Serial0/0/1
172.30.0.0/16 is variably subnetted, 2 subnets, 2 masks
C 172.30.30.0/24 is directly connected, FastEthernet0/1
L 172.30.30.1/32 is directly connected, FastEthernet0/1

## Slide 8
R1
R2
R3
10.1.1.0/30
10.2.2.0/30
.1 F0/1
172.30.10.0/24
.1 S0/0/0
.2 S0/0/0
.2 S0/0/1
.1 S0/0/1
172.30.30.0/24
.1 F0/1
Network Topology
209.165.201.0/24
.1 F0/0

## Slide 9: Questions - R2 Routing Table
What does variably subnetted mean ?
  Using VLSM
R 172.30.0.0/16 [120/1] via 10.2.2.1, 00:00:23, Serial0/0/1
[120/1] via 10.1.1.1, 00:00:09, Serial0/0/0
  What does R tell Us ?
    Routing protocol is RIP
  What does [120/1] tell Us ?
    120 Administrative Distance
    Hop Count
  What does 00:00:23 tell Us ?
    7 secs until next update
  Why are RIP updates from 172.30.0.0/16 coming from two different interfaces ?
    R1 and R2 have 172.30.0.0 subnets
Notes: 2.2.1.6 Verify a Static Route

## Slide 10: Questions – R1 Routing Table
R1 cannot see the 172.30.30.0/24 subnet, Why ?
    By default, routing protocols summarize to the class level eg 172.30.0.0/16, hence no subnet information is passed, when an update is sent to another network 10.0.0.0/8
Notes: 2.2.1.6 Verify a Static Route

## Slide 11: Questions – R1and R3 Routing Table
  R1 and R3 cannot see network 209.165.201.0/24, Why ?
    R2 did not advertise this network
Notes: 2.2.1.6 Verify a Static Route