## Slide 1: Network Topology Exercise C V1.0
Overview
You have been given the routing tables of six routers: Melbourne, Sydney, Perth, Hobart, Darwin and Adelaide
Given the information provided in each of the router’s routing table you will be required to complete the following tasks:
  Create a Network Topology Diagram, refer page 2
  Answer questions, refer page 6, regarding the Topology Diagram and Routing Tables

## Slide 2: Task 1 - Create a Network Topology Diagram
Refer to the sample Network Topology Diagram Layout below, your answer must conform with the Drawing Symbols and Layout.
Refer to the Routing Tables, which contain the information needed to create your diagram.
On your diagram show the following:
  all interfaces, serial, fastethernet and loopback, on each router
  all Links - serial links between routers and links to LANs
  all network addresses with prefix
Rx
Rx
Serial Link
LAN Link
S0/0/0
S0/0/1
Fa0/0
Fa0/1
LAN Link
Network Address/Prefix
Network Address/Prefix
Network Address/Prefix
Task 1 - Network Topology Diagram Layout
Loopback 0
ip address/prefix

## Slide 3
Melbourne Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default
Gateway of last resort is not set
105.0.0.0/28 is subnetted, 1 subnets
C 105.1.1.0 is directly connected, FastEthernet0/0
165.5.0.0/30 is subnetted, 1 subnets
C 165.5.5.0 is directly connected, Serial0/0/0
S 172.16.0.0/16 is directly connected, Serial0/0/0
Perth Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default
Gateway of last resort is 172.16.40.105 to network 0.0.0.0
172.16.0.0/16 is variably subnetted, 7 subnets, 5 masks
C 172.16.0.0/19 is directly connected, FastEthernet0/0
D 172.16.36.0/23 [90/2172416] via 172.16.40.102, 00:09:40, Serial0/0/0
D 172.16.39.0/24 [90/2172416] via 172.16.40.102, 00:04:53, Serial0/0/0
D 172.16.40.64/27 [90/2297856] via 172.16.40.105, 00:22:55, Serial0/0/1
D 172.16.40.96/30 [90/2681856] via 172.16.40.105, 00:22:11, Serial0/0/1
C 172.16.40.100/30 is directly connected, Serial0/0/0
C 172.16.40.104/30 is directly connected, Serial0/0/1
D*EX 0.0.0.0/0 [170/7289856] via 172.16.40.105, 00:00:52, Serial0/0/1
Routing Tables
Sydney Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default
Gateway of last resort is 0.0.0.0 to network 0.0.0.0
165.5.0.0/30 is subnetted, 1 subnets
C 165.5.5.0 is directly connected, Serial0/0/1
172.16.0.0/16 is variably subnetted, 7 subnets, 5 masks
D 172.16.0.0/19 [90/2172416] via 172.16.40.106, 00:22:14, Serial0/2/0
D 172.16.36.0/23 [90/2684416] via 172.16.40.106, 00:08:59, Serial0/2/0
D 172.16.39.0/24 [90/2684416] via 172.16.40.106, 00:04:11, Serial0/2/0
C 172.16.40.64/27 is directly connected, Loopback0
C 172.16.40.96/30 is directly connected, Serial0/1/1
D 172.16.40.100/30 [90/2681856] via 172.16.40.106, 00:18:28, Serial0/2/0
C 172.16.40.104/30 is directly connected, Serial0/2/0
S* 0.0.0.0/0 is directly connected, Serial0/0/1

## Slide 4
Darwin Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default
Gateway of last resort is 172.16.40.101 to network 0.0.0.0
10.0.0.0/30 is subnetted, 1 subnets
C 10.10.10.0 is directly connected, FastEthernet0/1
172.16.0.0/16 is variably subnetted, 7 subnets, 5 masks
D 172.16.0.0/19 [90/2172416] via 172.16.40.101, 00:21:04, Serial0/1/1
C 172.16.36.0/23 is directly connected, FastEthernet0/0
S 172.16.39.0/24 is directly connected, FastEthernet0/1
D 172.16.40.64/27 [90/2809856] via 172.16.40.101, 00:21:04, Serial0/1/1
D 172.16.40.96/30 [90/3193856] via 172.16.40.101, 00:21:04, Serial0/1/1
C 172.16.40.100/30 is directly connected, Serial0/1/1
D 172.16.40.104/30 [90/2681856] via 172.16.40.101, 00:21:04, Serial0/1/1
D*EX 0.0.0.0/0 [170/7801856] via 172.16.40.101, 00:04:41, Serial0/1/1
Adelaide Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default Gateway of last resort is not set
10.0.0.0/30 is subnetted, 1 subnets
C 10.10.10.0 is directly connected, FastEthernet0/0
172.16.0.0/24 is subnetted, 1 subnets
C 172.16.39.0 is directly connected, FastEthernet0/1
Hobart Routing Table
Codes: C - connected, S - static, R – RIP, D - EIGRP
* - candidate default
Gateway of last resort is 172.16.40.97 to network 0.0.0.0
172.16.0.0/16 is variably subnetted, 6 subnets, 4 masks
S 172.16.0.0/19 is directly connected, Serial0/0/1
S 172.16.36.0/23 [1/0] via 172.16.40.97
C 172.16.38.0/24 is directly connected, FastEthernet0/1
S 172.16.39.0/24 is directly connected, Serial0/0/1
C 172.16.40.0/30 is directly connected, FastEthernet0/0
C 172.16.40.96/30 is directly connected, Serial0/0/1
S* 0.0.0.0/0 [1/0] via 172.16.40.97
Routing Tables

## Slide 5
Adelaide
Perth
Hobart
Sydney
Darwin
Task 1 - Network Topology Diagram
Melbourne
172.16.0.0/19
S0/0/0
S0/0/1
165.5.5.0/30
172.16.40.64/27
Loopback 0
f0/0
105.1.1.0/28
S0/2/0
S0/0/1
172.16.40.104/30
S0/1/1
S0/0/0
S0/1/1
S0/0/1
F0/1
F0/0
F0/1
F0/0
F0/1
F0/0
172.16.38.0/24
172.16.40.100/30
172.16.40.96/30
10.10.10.0/30
172.16.39.0/24
172.16.36.0/23
172.16.40.0/30
F0/0

## Slide 6: Task 2 – Topology Diagram and Routing Tables Questions
  List the routers that use EIGRP Sydney, Perth, Darwin
  On Hobart how many static routes are mapped to exit interfaces and how many to next hop IP addresses? Exit interface 2, next hop 2
  List the routers that use only static routes Melbourne, Hobart
  What is the IP address on S0/1/1 on Sydney router? 172.16.40.97
  List the routers that learn their gateway via EIGRP Perth, Darwin
  List the routers that use a static route to point to the gateway Melbourne
  Which router is the gateway router? Sydney
  Which router is the ISP? Melbourne
  On Darwin what does [90/3193856] mean and on Hobart what does [1/0] mean?
  On Sydney what does 00:08:59 mean? Time since last update

## Slide 7: Task 2 – Topology Diagram and Routing Tables Questions
  EIGRP is configured on Adelaide, what can be a reason why the routes to the rest of the network are not present in its routing table? No auto summary has to be configured for the routing protocol
  List the routers that have loopback interfaces? 172.16.40.64/27 Loopback 0
  A packet is sent from Darwin to Melbourne, what will be the exit interface on Darwin and the next hop IP address for this packet? exit interface S0/1/1, next hop address 172.16.40.101
  What are the IP addresses of the interfaces on Perth s0/0/1 172.16.40.16, s0/0/0 172.16.40.101 f0/0 172.16.0.1