## Slide 1: In Lab Scenario 4 2022 V1.2
Student ID:
Student Name:
Session Time:
Tutor’s Name:

## Slide 2
Latur
(Internal)
Router
R1
Latur
Switch S3
3650
Your Address Space
145.VZ.0.0/18
In Lab Scenario 4 - OSPF, ACLs, 4R V1.2
G0/1
S0/1/1
S0/1/0
OSPF Routing Protocol
Barshi
(Gateway)
Router
R3
G1/0/11
ISP
Router
R4
Inter-VLAN
Routing
ISP Link
Network Address
201.11.5W.0/30
PC1
VLANXXX
PC2
VLANYYY
G1/0/13
Fa 0/24
Internal Serials
Loopback 0
Server LAN
Database Server
Network Topology
S0/2/0
S0/1/0
A Network Configuration and Trouble Shooting Scenario
Internal
External
Connection to rest of
Internal network
Udgir
(Internal)
Router
R2
Udgir
Switch S2
2960
Inter-VLAN
Routing
G0/0/1
G0/0/1
S0/1/1
S0/1/1
S0/1/0
S0/1/0
182.18.0.0/16
Packet Tracer
External
Server-PT
Server0
Ethernet Interface
Or
Loopback 0
If in Lab Router
Packet Tracer
External
Server-PT
121.0.0.0/8
Server1
Ethernet Interface
Or
Loopback 1
If in Lab Router
Loopback 2
141.66.0.0/16
External Network
Loopback 3
217.2.45.0/24
External Network
“The Internet”
PC Ethernet VM
If in lab
PC VAN VM
If in lab

## Slide 3: The Scenario – An Analytical and Systematic Approach
The aim of this approach is to allow you to integrate the different topics (theory and practical) covered in the Unit, into the building of the network platform.
Each scenario requires you to build a working network, then add new network services and functionality to the network platform.
It is designed to be self re-enforcing, as what you have learnt in previous scenarios is required in future scenarios.
It emphasizes an Analytical and Systematic approach to building the network platform:
  Produce a Network Topology
  Prepare the VLSM Design
  Follow a step-by-step process to ensure that, configuration, testing, and troubleshooting is done in an order and sequence that will achieve a working network.
Doing the scenarios will prepare you for the Skills Tests
  Your tutor will provide advice and feedback only during your on campus Lab Session

## Slide 4
Scenario 4 - Introduction
This scenario can be completed independent of the lecture material as configuration details are provided on pages 15 to 26
Your instructor will give you an overview of the scenario at the beginning of the lab
As a How to Configure Guide, it is recommended you obtain a copy of “CCNA Portable Commands Guide (CCNA Self-Study) 2/3/4/5 Ed”, Scott Empson, Cisco Press
What is new?
  You will configure OSPF (Open Shortest Path First) Routing Protocol on the routers
  ACLs to control pings between subnets
Network Topology
  Internal, your internal network
  External, the link to the ISP and the Internet
  Use following Network addresses for Scenario 4, refer page 5 to determine V, Z and W
    The Corporate Network Address, 145.VZ.0.0/16.
    The corporate address has been divided up and you have been given a part of the address space 145.VZ.0.0/18 to build your section of the Corporate Network.
    Do not configure the connection to the rest of the internal network
    ISP Link Address, 201.11.5W.0/30

## Slide 5
How to determine your Network Addresses and VLAN Numbers
Rule Set B
Network Addresses (Example Only, use your student ID)
  eg student Id
    Nine digit Id 123057210 (Left to Right)
    If Seven digit Id 3057210 then 993057210 (from Left to Right)
  Rule 1: If the Corporate Network Address is 145.VZ.0.0/16 where V is seventh number and Z is fifth number in your student ID
    V=2 and Z=5, hence 145.25.0/18 is your Corporate Network Address
  Rule 2: If the ISP Link Address is 201.11.5W.0/30 where W is eighth number in your student ID
    W=1, hence 201.11.51.0 is your ISP Link Address
VLAN Numbers – (Example Only, use your Student ID
  eg student Id
    Nine digit Id 123057210 (from Left to Right)
    If Seven digit Id 3057210 then 993057210 (from Left to Right)
  Rule 1: VLAN XXX where XXX are the fifth, sixth and seventh numbers in you student ID
  Rule 2: VLAN YYY where YYY are the sixth, seventh and eighth numbers in you student ID
  Rule 3: IF XXX = YYY then XXX = XXX + 1
  Rule 4: VLAN 154 , IF XXX or YYY = 154 then 154- 3 = 151
  Appling Rules
    Rule 1: VLAN XXX: XXX= 572 hence VLAN572
    Rule 2: VLAN YYY: YYY=721 hence VLAN721
    Rule 3: No need to apply
    Rule 4: No need to apply

## Slide 6
Scenario 4 Addresses and VLAN Numbers
Record your Network Addresses and VLAN Numbers
Refer Rule Set B
Your Student ID:
Your section of Corporate Network Address space 145.VZ.0.0/18 V = Z =
    Your ISP Link Address 201.11.5W.0/30 W =
Your VLAN Numbers

## Slide 7: Task 2 VLSM Design – Use VLSM Calculator Paste Below

## Slide 8: Scenario 4 -Tasks
1. Do not configure enable passwords OR line console passwords on router and switches, unless specified by the task
2. Internal Network VLSM Design – Paste in page 7
a) Design IP VLSM Addressing Scheme with:
  Refer rules page 5
  Switch S3 VLAN XXX Orange 400 hosts
  Switch S3 VLAN 1 18 hosts
  Switch S2 VLAN YYY White 140 hosts
  Switch S2 VLAN 154 Grey 68 hosts (154 may change, refer rules page 5)
  Switch S2 VLAN 1 12 hosts
  Barshi Database Server LAN loopback 0 20 hosts
  3 Internal Serials 2 hosts each
b) Document assignment of ip addresses to router interfaces and PC Hosts
c) Use a VLSM calculator
3. Cable Connection
a) Connect Latur router G0/0/1 to Latur switch 3 port G1/0/11
b) Connect Udgir router G0/0/1 to Udgir switch 2 port G0/1
c) Check routers are connected via serial links
d) Connect PC1 to G1/0/13 S3 using the patch panel in Lab or directly to G1/0/13 S3 in Packet Tracer, connect PC2 to Fa 0/24 S2 using the VAN in Lab or directly to Fa 0/24 S2 in Packet Tracer
e) Connect Packet Tracer Servers to ISP via ethernet cables
4. Helpful Configurations
a) Configure the line console on each router and switch, as shown below:
line console 0
logging synchronous (stops system messages overwriting your typing)
exec-timeout 0 0 (ensures you do not return to user executive mode)
b) Turn off DNS (Domain Name Service)
no ip domain-lookup (ensures if you miss-type a command, the router will not try to resolve the command as a URL web address)
5. Message of the Day (MOTD) Banner Configuration
You must configure a MOTD Banner, recording your student id, family name and session time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Session Time
&
6. Device Host Names
a) All devices must be configured with a host name eg LaturR1, LaturS1 etc

## Slide 9: Scenario 4 -Tasks
7. Switch Configuration
a) Refer to pages 22 to 25 and to your journal and lab exercises from prior unit on Basic Switch and VLAN Configuration
b) Check the switch is clean, if NOT then:
i) Delete the vlan.dat file to remove old VLANs from the Switch, use - delete vlan.dat
ii) Use - erase startup-config then reload
c) On switch S3 3650
  create VLAN XXX Grape
  Configure switch ports G1/0/13, G1/0/14 as VLAN XXX access ports
  configure Port Security, mac address sticky on ports G1/0/13, G1/0/14, max 2, with violation protect
d) On Switch S2 2960
  Create VLAN YYY White, VLAN 154 Grey (154 may change, refer rules page 5)
  Configure port 24 as VLAN YYY access port
  If Lab Kit - Configure a static mac address on port 24 use the MAC address of PC2
  If Packet Tracer - configure Port Security, mac address sticky on port 24 max 1, with violation shutdown
e) On S3 switch configure G1/0/11 as a trunk port, On S2 switch configure G0/1 as a trunk port.
f) Switch Management – on both switches configure an ip address on interface VLAN 1 and configure a default gateway
g) Configure enable password cisco and Line vty with password cisco and login, so each switch can be configured via Telnet
8. Trouble Shooting VLANs
a) To check VLANs created, use – show vlan brief
9. Trouble Shooting Port Security
a) To check port security is enabled, use - show port-security
b) A table will be displayed showing the security status of the switch ports
10. Network IP Address Configuration
a) Configure ALL router serial and loopback interfaces with ip addresses and descriptions
b) Configure Packet Tracer Servers with ip addresses, connect to ISP via ethernet cable
c) Latur and Udgir Router
i) Refer page 21 and to your journal and lab exercises from prior unit on Basic Inter-VLAN Routing
ii) Configure Inter-VLAN routing on G0/0/1
  - Latur configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN XXX
  - Udgir configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN YYY
  - Configure each sub-interface with an ip address
d) Configure PC1 and PC2 Hosts with specified VLAN
i) IP address and subnet mask.
ii) Default Gateway IP address.
e) Check default gateways configured on switches

## Slide 10: Scenario 4 -Tasks
11. Trouble Shooting Trunking – between Switch and Router
a) To check Trunking is activated, on switches, use – show interface trunk
b) Check correct interface has been configured for trunking !
12. Trouble Shooting Point-to-Point Single Link Testing
a) This test is to check that each individual link in the network is working.
b) Ping (command) – ensure you can ping from one end of each link to the other:
  PC to Router in same subnet/VLAN/network.
  PC to PC in same subnet/VLAN/network.
  Router to each direct neighbour Router over a serial link.
c) Link NOT working ? - Common problems:
  Physical connection not made.
  The clock rate is not configured on DCE interface of a serial link.
  An incorrect IP address or subnet mask is configured on one interface of a link
  The interface is shutdown.
13. Trouble Shooting Inter-VLAN Routing Testing
a) This test is to check Inter-VLAN routing is working
b) Ping PC1 – VLAN XXX to ip address of Latur Switch 1
c) Telnet PC1 – VLAN XXX to ip address of Latur Switch 1
d) Ping PC2 – VLAN YYY to ip address of Udgir Switch 2
e) Check IP address/Mac address mapping on the router, show arp
14. Routing Protocol Configuration (refer page 18-20)
a) Latur and Udgir
  OSPF using wildcards for each subnet
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
b) Barshi
  OSPF using wildcards for each subnet
  Do not advertise the external network address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to other internal Routers
c) ISP Router
  Do not configure OSPF
  Only configure a static route (default class B mask) to your internal network
  Configure loopbacks and Packet Tracer Server Devices

## Slide 11: Scenario 4 -Tasks
15. Trouble Shooting OSPF Neighbor Adjacency
a) Verify that the routers have formed an adjacency with each other, use - show ip ospf neighbor
b) Adjacency NOT Formed ? - If an adjacency has not formed it could be due to:
i) subnet masks on each end of link do not match
ii) the directly connected network is not included in the network statements
c) Other trouble shooting commands: show ip protocols, debug ip ospf packets
16. Trouble Shooting Routing - Presence of Subnets
a) Internal Routers
- Use show ip route to display the routing table on each router:
- Check all the subnets are present
- Check there is a default route
b) ISP Router
- Use show ip route to display the routing table:
- Check there is static route back to your internal network
c) Common problems:
  Routing protocol is not advertising a subnet
  An interface is down
  Static or Default route not configured
17. Trouble Shooting End-to-End Path Testing
a) This test is to check that the routing - static and dynamic, is working.
b) Ping from PC1 in VLAN XXX to PC2 in VLAN YYY
c) Ping from PC Hosts in VLAN XXX and VLAN YYY to External Web Server and the Internet
d) Use traceroute to pin point problems.
e) Use debug ip icmp on ISP router to check ping request arrives
f) Check if a subnet is missing from a routing table, use - show ip route
g) End-to-End Path Test Failed ? - Common problems:
  Default gateway IP address not configured on a PC.
  PC connected to incorrect interface.
  Incorrect static route on ISP
  Subnet not advertised
  Default route not propagated

## Slide 12: Scenario 4 - Tasks
18. OSPF Link Bandwidth Settings
a) Link Barshi to Udgir configure bandwidth 512
b) Link Latur to Barshi configure bandwidth 128
c) Link Latur to Udgir configure bandwidth 512
d) Check routing table in each router, use - show ip route, are the best routes shown ?
19. Link State Database Have a Look
a) On an internal router, use – show ip ospf database
20. Trouble Shooting Back Up Link Testing
a) On Latur router, check that if exit interface to ISP is shutdown a back up will appear in the routing table.
21. HTTP Servers
a) On In Lab Routers
  Configure a HTTP server on ISP Router, use – ip http server
b) Packet tracer
  If you are using Packet Tracer you must configure Web Servers and connect the servers to the ISP Router
c) Allows you to test your ACLs using a Browser.
22. Telnet Access to Routers
a) Configure line vty with password cisco and login, so you can connect to each router can via Telnet
b) NO enable password is required as you are NOT configuring the router
c) This allows you to test your ACLs using Telnet.

## Slide 13: Scenario 4 - Tasks
23. Access List Requirements
a) Refer to pages 15 to 17 and Lab Exercises on Access Control Lists
b) You must create a NAMED Extended ACL for VLAN XXX based on following requirements:
  PCs in VLAN XXX permitted HTTP access to ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router and denied ALL other access to this Server.
  PCs in VLAN XXX permitted ALL access to the Internet – all the other Servers.
  ALL means IP
c) You must create a NAMED Extended ACL for VLAN YYY based on following requirements:
  PCs in VLAN YYY denied PING access to PCs in VLAN XXX
  PCs in VLAN YYY permitted ALL access to the Internet. The Internet is represented be a single Loopback for testing, your ACL must allow access to all addresses in the Internet
  ALL means IP
d) You must create NAMED Standard ACLs to control Telnet access to the routers based on following requirements:
  ONLY PCs in VLAN XXX permitted TELNET access to Latur Router
  ONLY PCs in VLAN XXX denied TELNET access to Barshi Router
e) You need to be analytical and systematic in our approach to translating the above requirements into a set of rules – the ACL statements, which
then must be tested to ensure the above requirements have been satisfied:
i) Create NAMED Extended ACLs for VLAN XXX and VLAN YYY using the template on page 17, refer Task 24
ii) Test the NAMED ACLs for VLAN XXX and VLAN YYY refer Task 25
iii) Create NAMED Standard ACLs for Telnet access using the template on page 18, refer Task 24
iv) Test the NAMED ACLs for Telnet access refer Task 25

## Slide 14: Scenario 4 - Tasks
24. Creating and Configuring NAMED Access Lists
a) Refer Lab Exercises on Access Control Lists
b) Use Notepad to create your ACLs, note ACL names are case sensitive eg aclvanXXX and AclvlanXXX are different acls
c) Identify each requirement then configure an ACL rule for each requirement.
d) Create a NAMED access list in Notepad, consider the ordering of the rules, use the following structure:
! Deletes previous version of access list
no ip access-list extended ACLVLAN<Id>
! Insert Latest version of access list
ip access-list extended ACLVLAN<Id>
<Your ACL rules>
! For most situations this should be the last rule ie permit all other access to “The Internet”
permit ip any any
e) Combine ACL rules as required to form your access list, carefully consider the order in which the rules should be arranged.
f) Paste ACL from Notepad into router (router must be in global configuration mode)
g) Configure ACL on correct interface
25. Trouble Shooting Access Lists
It is important to verify that the ACL rules actually work as intended, refer to the steps below:
  1. Use show access-lists
    If all rules tested go to 5
    Else Identify which rule you want to test
  2. Use clear access-list counters
    Clear any counts against the rules
  3. Go to PC in VLAN<Id> perform test eg Ping, Telnet, Browser etc to trigger a match with the identified rule
  4. Use show access-lists
  Was the identified rule matched ?
    Yes – rule action correct, Repeat process, go to 1
    No – Debug
      Was another rule matched ?
      Where no rules matched ?
      Check syntax and order of rules – make changes (in Notepad, then paste into config) – Repeat process go to 1
5. Trouble Shooting completed

## Slide 15: Scenario 4 – ACL Templates
ACL for VLAN XXX on Latur Router
The Access List – Extended Named (create in Notepad, then paste into router config mode)
no ip access-list extended ACLVLANXXX (Delete previous version of the ACL for VLAN XXX )
Ip access-list extended ACLVLANXXX (Self-documenting, the ACL for VLAN XXX)
! Only permit HTTP access to the ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router ( ! means comment)
permit tcp source subnet wildcard host ip address eq www
! Deny ALL other access to the ISP Packet Tracer Server0 or ISP Loopback 0 if in Lab Router
deny ip source subnet wildcard host ip address
! Permit access to The Internet
permit ip any any
ACL Placement - On Sub Interface G0/0/1.XXX on Latur Router
interface G0/0/1.XXX
ip access-group ACLVLANXXX in
ACL for VLAN YYY on Udgir Router
The Access List – Extended Named (create in Notepad, then paste into router config mode)
no ip access-list extended ACLVLANYYY (Delete previous version of the ACL for VLAN YYY )
Ip access-list extended ACLVLANYYY (Self-documenting, the ACL for VLAN YYY)
! Deny PING access to a destination - PCs in VLAN XXX subnet
deny icmp source subnet wildcard destination subnet wildcard
! Permit access to The Internet
permit ip any any
ACL Placement - On Sub Interface G0/0/1.YYY on Udgir Router
interface G0/0/1.YYY
ip access-group ACLVLANYYY in

## Slide 16: Scenario 4 – ACL Templates
ACL to control Telnet Access to Latur and Barshi Routers
The Access List – Standard Named (create in Notepad, then paste into router config mode)
! On Latur
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Permit VLANXXX Telnet Access to Latur
permit source subnet wildcard (inverse of subnet mask)
deny any
! On Barshi
no ip access-list standard ACLTELNET
ip access-list standard ACLTELNET
! Deny VLANXXX Telnet Access to Barshi
deny source subnet wildcard (inverse of subnet mask)
permit any
Interface Placement - line vty 0 4, on Latur and Barshi Routers
line vty 0 4
password cisco
login
access-class ACLTELNET in

## Slide 17: Scenario 4 – ACL Overview
Case Sensitivity
ACL names are case sensitive eg aclvlan361 and AclVlan361 are different ACLs
Should decide to use either all uppercase - ACLVLAN361 or all lowercase – aclvlan361 names to reduce errors
Placement Rules
Standard ACL – place as close as possible to destination network or device, to avoid unnecessarily blocking traffic
Extended ACL – place as close as possible to source network or device, to block traffic early to reduce congestion
Trouble Shooting Commands
show access-lists (shows all access lists)
clear access-list counters (clears ip packet hits against a rule)
Trouble Shooting Commands
show access-lists (shows all access lists)
clear access-list counters (clears ip packet hits against a rule)
Use the following to test the rules: ping, telnet, a browser

## Slide 18: Routing Configuration Rules
Each router should only advertise its internal directly connected networks
Routing updates must not be sent to LANs/VLANs
A default route to the Internet should only be configured on the gateway router
Only the gateway router must advertise the default route to the internal routers
The ISP router should have a static route pointing to the corporate’s Network with the relevant class A, B, C mask
Do not configure the ISP router with a routing protocol advertising the corporate’s network

## Slide 19: OSPF Configuration
Configure on Latur Router
router OSPF 1 (1 is just a process id, for OSPF routers may use different process ids)
network ?.?.?.? ?.?.?.? area 0 (VLAN XXX, ospf routers exchange updates with routers in the same area)
network ?.?.?.? ?.?.?.? area 0 (VLAN 1 wildcard is inverse of subnet mask, ? means replace)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Latur to Barshi)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Latur to Udgir)
Passive Interface Options:
passive-interface G0/0/1.83 (Do not send routing information to LAN subnets)
passive-interface G0/0/1.XXX (Do not send routing information to LAN subnets)
OR
passive-interface default (Configure passive interface as default for all interfaces)
no passive-interface S0/1/0 (Configure S0/1/0 to allow the flow of routing information)
no passive-interface S0/1/1 (Configure S0/1/1 to allow the flow of routing information)
Configure on Udgir Router
router OSPF 2
network ?.?.?.? ?.?.?.? area 0 (VLAN YYY, ospf routers exchange updates with routers in the same area)
network ?.?.?.? ?.?.?.? area 0 (VLAN 1 wildcard is inverse of subnet mask, ? means replace)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Udgir to Barshi)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Udgir to Latur)
passive-interface G0/0/1.83 (Do not send routing information to LAN subnets)
passive-interface G0/0/1.YYY (Do not send routing information to LAN subnets)

## Slide 20: OSPF Configuration
Configure on Barshi Router
router OSPF 3
network ?.?.?.? ?.?.?.? area 0 (Loopback Database LAN)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Barshi to Latur)
network ?.?.?.? ?.?.?.? area 0 (Serial Link – Barshi to Udgir)
ip route 0.0.0.0 0.0.0.0 exit interface or next hop ip address (The default route to the Internet)
default-information originate (Advertise default route to other internal routers)
passive-interface loopback0 (Do not send routing information to Server LAN)
Configure on ISP Router (OSPF is not configured in ISP)
ip route ?.?.?.? ?.?.?.? exit interface or next hop ip address (ISP configure a static route to internal network)

## Slide 21: Inter-VLAN Routing Configuration
Configure on the required Router
interface G0/0/1
description The Physical Interface
no shutdown
interface G0/0/1.1
description A logical Sub Interface
description VLAN 1 Management
encapsulation dot1q 1
ip address <dotted decimal> <subnet mask>
interface G0/0/1.<vlan id>
description A logical Sub Interface
description VLAN <vlan Id> <vlan name>
encapsulation dot1q <vlan id>
ip address <dotted decimal> <subnet mask>
etc ……

## Slide 22: Switch Configuration
Switch S3 Configure VLANs
vlan XXX
name Orange
Switch S2 Configure VLANs
vlan YYY
name White
vlan 154 (154 may change, refer rules page 5)
name Grey
Configure IP address for management vlan
interface vlan 1
ip address ip address mask (This allows the switch to be configured remotely via Telnet)
Configure Default Gateway
ip default-gateway ip address of router interface (Use VLAN 1 subinterface IP address)

## Slide 23: Switch Configuration
Configure a switch ACCESS port (note you can specify a range of switch ports):
interface fa 0/3 (or interface range fa 0/3 – 5)
switchport access vlan <number> (assigns port to a vlan)
switchport mode access (sets port to access, for PCs)
switchport port-security (enables port security, do not forget this command)
switchport port-security maximum 1 (maximum of 1 mac address(es) can stick)
switchport port-security mac-address sticky
switchport port-security violation shutdown (shuts down port, default when security turned on)
OR
switchport port-security violation protect (protects, but does not shut down the port)
Configure a static MAC address entry in Mac Address Table
mac address-table static AAAA.BBBB.CCC vlan YYY interface fa 0/24
(replace AAAA.BBBB.CCCC with the mac address of the PC)

## Slide 24: Switch Configuration
Configure a switch TRUNK port
2960 Series Switch
interface G0/1
switchport mode trunk (sets port to trunk)
3650 Series Switch
interface G1/0/11
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation
switchport mode trunk (sets port to trunk
3560 Series Switch
interface Fa0/1
switchport trunk encapsulation dot1q (must specify 802.1q encapsulation)
switchport mode trunk (sets port to trunk)

## Slide 25: Switch Commands
Managing the MAC Address Table
show mac address-table (displays entries in table)
show mac address-table dynamic (displays only dynamic entries in table)
clear mac address-table (deletes all entries from table)
clear mac address-table dynamic (deletes only dynamic entries from table)
Re-activating a switch port that has been violated
When a violation causes a switch port to block traffic, it must be re-activated
This is achieved by doing a shutdown then a no shutdown on the switch port, refer below:
interface fa0/10
shutdown
(wait until shutdown confirmed)
no shutdown

## Slide 26: Other Management Commands
How to save a Router/Switch configuration: copy run start
How to remove a Router/ Switch configuration: write erase, then reload (say no when asked if want to save the changes)
How to remove the VLAN configuration on a Switch: delete vlan.dat
Some show commands
  show ip interface brief: very important to know how to read the output
  show run: displays the running configuration file (check running settings)
  show start: displays the startup config file (check the settings that will take effect after a reboot)
  show version: IOS version, image file name, last rebooted, config-reg value, etc

## Slide 27: How to configure SSH – Secure Shell
1. Configure switch or router with a hostname:
hostname S3
2. Configure a local user account:
username labuser privilege 15 secret cisco (always use cisco as password)
3. Configure domain name:
ip domain-name scenario.lab
4. Configure SSH Certificate:
crypto key generate rsa general-keys modulus 1024
5. Configure Line vty
line vty 0 15 (4 for a router)
transport input SSH
login local
end

## Slide 28: PC Command Window Useful Trouble Shooting Commands
ipconfig
  Allows you check your PC’s addresses
  ipconfig /all
  ipconfig /? for help
  To request the DHCP server to release or renew the PC’s IP address use:
    ipconfig /release, ipconfig /renew
netstat
  Displays the TCP/IP network protocol statistics and information
  netstat –a
  netstat –e
  netstat –s
  netstat /? for help
nbtstat
  Displays protocol statistics and current TCP/IP connections
  nbtstat –n
  nbtstat /? for help

## Slide 29: PC Command Window Useful Trouble Shooting Commands
arp
  Displays the Address Resolution table
  arp -a
  arp /? for help
route print
  Displays the routing table of your PC
  route /? for help
ping
  ping 127.0.0.1 Checks your PC’s IPv4 Protocol stack
  ping 192.168.1.10 ping a destination
  ping /? for help
tracert
  Traces individual hops to the destination
  tracert 192.168.1.10
  tracert /? for help